1.31um & 1.55um DFB-Laser Module

- Features

a. InGaAsP/InP MQW DFB LD

b. Low Threshold Current

c. High Reliability

d. High Output Power

e. Built-in Optical Isolator

- Applications

a. Data Communication

b. Video Transmission

c. CATV System

# ■Characteristics (1310nm & 1550nm Series)

(Tc=25℃)

| Parameter | Symbol | Unit | Test conditions | Min | Typ | Max |
| --- | --- | --- | --- | --- | --- | --- |
| Threshold Current |  | mA | CW | - - - 1290 1530 | 6 | 20 |
| Operating Current | Iop | mA | CW |  | 18 | 40 |
| Operating Voltage | Vop | V | CW, =Iop (Note 1) |  | 1.1 | 1.8 |
| Peak Wavelength | λc | nm | CW, IF=Iop |  | 1310 | 1330 |
|  |  |  |  |  | 1550 | 1580 |
| Spectral Width | Δλ | nm | CW, IF=Iop | - | - 1.0 |
| Output Power | PF | mW | CW, IF=Iop | - | 2.0 | - |
| Rise and Fall times | tr, tf | ns | =,10~90% (Note2) | - | 0.2 | - |
| Tracking Error | Er | dB | Tc= -40 ~ +85℃（PT3X53） Tc= 0 ~ +70℃（PT3X63） APC (Note 3) | - | 0.5 | 1.0 |
| Side Mode Suppression Ratio | SMSR | dB | CW, IF=Iop | 30 | 40 - |
| Monitor Current |  | mA | CW, IF=Iop , =5V | - | 0.2 | - |

Note 1. : Forward Current

2. : Bias Current

3. Er=MAX |10×log ( Pf (Tc) / Pf (25) ) |

# Optical isolator specification (PT3X63 Series)]

# Absolute Maximum Ratings

(Tc=25℃)

| Parameter | Symbol | Rating | Units |
| --- | --- | --- | --- |
| Storage Temperature | Ts | -40~+85 | ℃ |
| Operating Case Temperature | TC | -40~+85（PT3X53） 0~+70（PT3X63） | ℃ |
| Reverse Voltage (Laser diode) |  | 2 | V |
| Reverse Voltage (Photodiode) |  | 20 | V |
| Forward Current (Photodiode) |  | 2 | mA |

# Ordering information